## Slide 1: Sequenza di partenza dei Task
La sequenza di partenza dei Tasks non dipende da come questi vengono messi all’interno della funzione taskMain_loadTaskList, ma segue quest’altra sequenza per la quale un task, prima di partire, può aspettare che 1 o più tasks siano stati avviati:
Task Internal Bus
Task Network Interfaces
Task Timezone -> wait task 2 init
Task Alarms / DMD / Minimal Datalogger -> wait tasks 1, 2, 3 init
Task Web Server -> wait tasks 1, 2, 3, 4 init
Task Modbus Slave Measurer -> wait tasks 1, 2, 3, 4 init
Task Display ???

## Slide 2
Task
Alarms & DMD
Task
Web Server
Task
Internal Bus
(Measure Module)
Alarms Settings
Metering Settings: DMD Parameters
All physical values
(ex. Current, voltage, power, energy, etc.)
Task
Network Interfaces
(Ethernet, Wi-Fi, etc.)
Settings -> Communication
Ethernet parameters
Wi-Fi (softAP, station) parameters
mDNS parameters
Task
Timezone
Settings -> General:
NTP parameters (RTC Synchronization)
Task
Auxiliary Functions
(Check Wiring)
Task Modbus Slave Measure
Modbus RTU
Modbus TCP

## Slide 3
App main
Task Modbus Slave Measure
ESP Timer Task
(ESP_TIMER_TASK)
Task used for the silent time
It is a software timer
uart_queue_task
RX Task: wait for a shared queue (xMbUartQueue) in order to handle the received packets and store them in a struct.
  xMBPortSerialInit()
  vUart_RXTask()
Reception of packet from …
IRQ Service ESP32
queues (incoming packets)
serialDriv_queue
(modbus callback function)
queue
Modbus Serial Driver Task acts as an interface between the Modbus stack and the Serial Driver
This task moves the queue element from here to the queue driver
Simulate the IRQ on barebone firmware
Modbus UART

## Slide 4
App main
Task Modbus Slave Measure
tcp_slave_task
(vMBTCPPortServerTask() )
Task in charge of handle TCP connections.
This task opens, close, and received information of the different TCP connections. Also send the received packets to the driver upper layers.
mbs_port_tcp_task
(mb_tcp_driver_start() )
modbus_tcp_interface_task(): This function pass the configuration parameters defined in mb_communication_info_t struct to the driver object and verifies that the parameters are ok.
Modbus TCP
Event
queue

## Slide 5
App main
Task
Network Interfaces
(Ethernet, Wi-Fi, etc.)
Driver (CGC)
Driver (CGC)
Driver (CGC)
Driver (CGC)
Wi-Fi (ESP32)
mDNS
(ESP32)
sysEvent
(ESP32)
Ethernet
(ESP32)